How to switch modem band on eWON with Q24

# Introduction
The Q24 Wavecom modem is a Quad band modem but it does not switch automatically.
In order to make it switch, a special command must be entered.
This is done in factory but can also be changed by a tricky procedure.
The 2 band ranges selectable here are:
900E – 1800 MHz	Rest of the world
850 - 1900MHz	US

# What is the modem type
The hardware modem type must be
14,15,16,17

# Modem command
The command used for switching is :

AT+WMBS=X

With X from this table:

The modem must be restarted after entering this command.

# What is the procedure for switching to 850-1900

Replace the Modem init string by:

AT&FE0&D2&C1+IFC=2,2;+CSNS=4;+WMBS=4

(currently you only have AT&FE0&D2&C1+IFC=2,2)

Then reboot the eWON. Wait until you have a network. If after 10 minutes
you still don't have a network, reboot once more and wait for network again.

Once you have the network, try the communication.

+WMBS=4 will select the 850/1900MHz,

The default WMBS value is 5.
The modem must be restarted after entering this command.