eWON connected to DF1 Half Duplex Network
# Introduction
This document will explain how to configure the different devices on the DF1 Half Duplex Network.
In our example we will interconnect 2 SLC500 and 1 eWON.
eWON can only be configured as DF1-Slave not as DF1-master device. That's why you need to configure 1 SLC as DF1-Master.
After these configurations, eWON will be able to poll data on the different PLC and to act as transparent Gateway EIP to DF1.

The DF1 Half Duplex Network is configured like this:
The SLC 500 DF1-Master has DF1 Address 1 and is connected to the DF1 Network using a RS232 to RS485 converter.
The SLC 500 DF1-Slave has DF1 Address 3 and is connected to the DF1 Network using a RS232 to RS485 converter.
The eWON has DF1 Address 2 and is connected to the DF1 Network using a straight RS485 cable (3,5,8).

# SLC500 Configuration
## DF1-Master
The SLC500 which will act as DF1 Master has to be configured like this:

- Select DF1 Half Duplex Master and set Node Address to 1
- Select the «Std.single msg. Per scan» Polling Mode
- In the Polling Ranges configure the different polling ranges. For our example we used Priority Low = 2 and Priority High = 3, to ask the DF1-Master to poll the eWON and the other SLC500.

## DF1-Slave
The SLC500 which will act as DF1 Slave has to be configured like this:

- Select DF1 Half Duplex Slave and set Node Address to 3
- Use the same Com settings (Baud, Parity, Error Detection ...) as for the DF1 Master device

# eWON Configuration
Set the eWON dip switches in RS485 mode (On,Off,Off,Off)
Configure the eWON DF1 IOServer like this:

- Use the same Com settings (Baud, Parity, Error Detection ...) as for the DF1 Master device
- Set the «eWON DF1 Address» to 2
- In the «Destination DF1 Address» enter the DF1 Address of the device you want to reach using the transparent gateway EIP to DF1 (for remote maintenance for example)
- Configure Topic A to poll on the SLC500 with DF1 address 1
- Configure Topic B to poll on the SLC500 with DF1 address 3
Create some tags to test the polling on the different SLC500: