How to upgrade the ADSL modem locally using eWON proxy

# Introduction

The upgrade must be done with the eWON connected locally
The ADSL modem must be working and the WAN connection must be active (permanent internet connection set to ADSL enabled).

# Upgrade steps

NOTE

In this example, the eWON is configured in 10.0.100.55
## Configure the eWON Proxy

You need to setup the eWON proxy like this to provide access to the ADSL Modem:

## Configure the WAN connection

The “problem” with the proxy is it is enabled only when the WAN connection is active.
Your WAN connection must be working and WAN enabled to allow the proxy to work

NOTE

The WAN connection must not mandatorily be configured to ADSL, it can also be configured on Modem for example, but it must be active and permanent.

## Execute the upgrade procedure

Connect to the ADSL modem using your web browser (Firefox tested) by entering the following URL:

http://YOUR_EWON_ADDRESS:1234/hag/emweb/lclImageUpgradeNS.htm

You must see the following page:

Selected the TEImage.bin file provided.
Then select “Upload”

IMPORTANT

The operation takes a long time (more than one minute), don't switch of the eWON or the WAN connection during that time.
At the end of the upgrade process you will receive the following notice from the mode:

You can now reboot the eWON (OFF/ON) to apply the new firmware.

## Verifying the current ADSL firmware version

You can check, before and after upgrade the current modem firmware version from the eWON status page

Diagnostic → Status → Info
The version number is provided after the VUL- prefix.