Server on Endian-DMZ

# Purpose
By design, Endian-for-eWON “bridges” the LAN corporate network and all VPN Clients. For usual Road Warriors usage, this bridge is not a problem, but for eWON permanently connected by GPRS to the Endian-for-eWON, this bridge implies that all broadcast messages travelling on the LAN corporate network will be sent also on each VPN Client through GPRS connections. As you pay for any GPRS traffic, these broadcast messages could cost a lot of money (one broadcast message will generate several GPRS communications).

VPN Clients on GPRS-EDGE connection don't want to be "bridged" with the LAN corporate network. Then, placing the Application Server on the ENDIAN-DMZ blocks all broadcast messages from the LAN.

# Application Server placed on Endian-for-eWON DMZ

Figure 1: Network topology
In this topology, the Application Server is connected on DMZ interface of the Endian-for-eWON and there is nothing plugged in the LAN interface.

# Endian-for-eWON configuration
## Network configuration

## VPN configuration

In each Accounts, check the “Push route to orange zone” to allow eWON and devices behind to reach the Application Server.

Also, defines the “Network behind client”.

## Firewall configuration
To allow the DMZ (orange) zone to get access to the VPN, you need to add a rule to allow “Orange to Green traffic”.

Don't use the “VPN firewall”.
# Application Server configuration
You need to tell to the Application Server where the LAN network is.
Either use the Endian-for-eWON as default Gateway or add a route to the Endian-LAN.