DualBand GSM antenna
# Antenna description

Electrical
Frequency	890-960 MHz 1710-1880 MHz
Impedance	50Ω
Type	Lambda/4
Gain	0 dB

Mechanical
Antenna Cover	Plastic
Color	Black
Weight	170 g
Height	68 mm
Hole diameter	15.5 mm
Sheet metal thickness	0.5 to 2.5 mm
Termination	Low loss RG 58 (2m) + FME fitted

A SMA/FME adapter is provided by “eWON sa” to connect antenna to eWON-SMA connector.