eSync - VPN Server configuration
# Introduction
eSync can also include an OpenVPN server.
By default the VPN server is not activated and not displayed inside eSync.
However, people wanting to combine the eSync Data management feature and the OpenVPN server on the same machine will be able to do this by going through this technical note.
# Configuration
## VPN Server configuration
To enable the VPN feature, follow the following procedure step by step :
1. Create an empty file named “esyncvpn.probe” in the <eSync directory>\WebSite.
2. Add or Update the TAP interface of the PC.

   To add the Tap interface, we provide two BAT files located in <eSync directory>\OpenVPN\drivers\x64 :
   install.bat and AddTap.bat.
   If your PC does not yet have a TAP interface, run the install.bat.
   If you PC already has one Tap interface, then run Addtap.bat.
   Both BAT files must be run with administration rights (right-Click → Run as Administrator)
3. Create the DH key for your server. For this, run the bat file create_dhpem.bat located in <eSync directory>\openvpn\config\
4. Start the service eSyncOpenVPNLauncher . You can do this using the command “net start eSyncOpenVPNLauncher”.
Warning	The service eSyncOpenVPNLauncher and the service OpenVPNLauncher provided by eCatcher and eGrabit cannot run at the same time.

Once this has been done, open the eSync configuration page by using the link “http://IP_of_eSync/initialsetup.php” inside your Web browser.
In this Window, you will find a form where you have to enter your personal information. These data will be used to generate the OpenVPN certificates for your VPN server. The options “Automatically create CA certificate” and “Automatically create the eSync Server certificate” must be checked. When it is correctly filled, click Next. eSync will generate the necessary certificates and go to the next configuration page.

This one allows you to configure your VPN server. You should see the two symbols that confirm the two certificates have been generated successfully.
Here is a description of all parameters to fill in this form :
Public Hostname (or IP)	Type the public hostname or Ip of your eSync server. This is the hostname/IP that eWON will use to connect the server in order to establish the VPN connection.
OpenVPN UDP Port	Type the UDP port that the server will use to listen for incoming connections.
eSync Server VPN IP	Type the IP address used by the server on the VPN network.
VPN DHCP Subnet Mask	Type the subnet mask of the VPN network. This mask combined with the VPN Server IP defines the network range of your VPN network.
VPN Static IP's Pool	Define a network range that is included in the global VPN network range. This network sub-range can be used for assigning static IP addresses to VPN clients. The other IP addresses outside this range but still included in the VPN network range will be used for assigning Dynamic IP addresses to VPN clients.
eWON LAN Pool	Define a network range for the LAN network of your eWONs. / If you want to connect to the eWON LAN from the VPN network, you must use a different network range for every eWON LAN. Defining a network range here, will help you select unique network ranges for your eWONs. (Ex : If you define here the range 10.9.0.0 , 255.255.0.0 , eSync will suggest the range 10.9.0.0 , 255.255.255.0 for the first eWON, 10.9.1.0 , 255.255.255.0 for the second eWON,...

When it is done, click the button start eSync and the VPN server should then start.
To check if it started successfully, verify that there are some logs appearing in the page “Main Menu → VPN Diagnostic”.

## eWON Configuration
### First declare the eWON inside eSync
When you edit an eWON in eSync, you get now additional parameters that help you to declare the eWON as a VPN client.

VPN Settings	Select whether you want to assign a static or a dynamic IP to your eWON. The static IP address range depends on the “VPN Static IP's Pool” parameter in the VPN server configuration (See System Setup menu)
LAN Settings	Define the network range of the eWON LAN. Remember that every eWON must have a different network range if you need to access the eWONs LAN through the VPN network.
Certificate	This menu allows to generate the certificate and the key for your eWON. If you see , then the certificate has not been generated yet and you must click “create” to generate it. At the opposite, if you see , then the certificate has already been generated. (See chapter 2.2.2)
Connection type	Check whether the eWON will connect through a GPRS connection or not. This will help to apply the right VPN KeepAlive parameter.

When everything is correctly filled, click “Add/Update”.
### eWON VPN configuration
Now your eWON has been declared in eSync, you need to configure the VPN connection in your eWON.
To achieve this you can use the eWON config export feature of eSync.

#### Configuration using Export Feature

This feature generates a comcfg.txt file with all connection parameters (IP, Certificates,...) already configured. Then, this file simply needs to be uploaded to eWON through FTP.
To generate the file in eSync, click “Configuration → eWONs Setup”. Then, select the eWON to export and click “Export Selected eWON”.

Make sure the file name is comcfg.txt and then, using FTP, push the file to the eWON root.
eWON should now contain the VPN keys and server information.
#### Manual Configuration

Instead of using the export feature explained here above, you can also configure the VPN server connection manually.
In eWON, go to System Setup → Communication → Network connections → VPN → Outgoing.

In this menu, you have to select “Defined manually” and type the IP/hostname of eSync. Depending on the topology, it could be the Public IP of the Internet router or the eSync Local IP.
Concerning the VPN Server settings, select “VPN Server “ and paste the eWON private key and certificate as well as the CA certificate in the right fields.
eWON private key and certificate can be extracted from eSync server by editing the eWON and click “edit”. (See 2.2.1)
CA certificate can be accessed in the eSync server folder “<eSync Directory>\OpenVPN\Certificates\keys”

## User Configuration
You probably also want to connect PCs and not only eWONs to your VPN network. This is also possible with eSync.
### First declare a User for the PC connection inside eSync
eSync users can also connect to eSync as a VPN client. To configure this, edit or create a user (Configuration → Users Setup).
You will see now that a new configuration menu appears :
Like for an eWON definition, this menu allows generating VPN certificate for your user. This is the only additional action to do.
### PC configuration
To configure the VPN client on the client machine, the software eGrabit is used. This software is available on http://wiki.ewon.biz/Support/07_Download/10_EWON_Softwares
In eGrabit, either you can declare your eSync Server manually or, like for an eWON, use the export feature of eSync.
For this, you just need to select the user to export and click “Export Selected User”.

You get an XML file that you can easily import in eGrabit.

# Router/firewall configuration
Your eSync server will probably not be directly visible on Internet, but will be installed behind a router or a firewall.
To allow the eWONs to connect to the eSync VPN server, you'll need to declare a Port forwarding rule on the router.
You should forward one UDP port to the local eSync IP address on port UDP 1194 (=port used for the VPN connection).
Remark: There is no need to create a rule for the HTTP port which will be used for the historical data transfer. The data transfer will be performed through the VPN tunnel.

# eWON Data Management configuration
As the eWON will now connect to the eSync server using a secured VPN tunnel, we will use this tunnel to send also the historical data through this tunnel.
For this, inside the Data management configuration of the eWON, instead of using the server URL we will use here the VPN IP address of the eSync Server (standard config = 10.8.0.1).

# Versions
The version of OpenVPN used by eSync is 2.3.4